## Slide 1: Impedance Matching Techniques
Impedance matching using :
Lumped elements
Quarter-Wave transformer
Single-Stub Tuner
Double-Stub Tuner
Impedance matching is necessary to provide maximum delivery of RF power to load from source

## Slide 2: BandWidth
Highest frequency of band, Hz
Lowest frequency of band, Hz
Design or center frequency, Hz

## Slide 3: λ/4 section bandwidth
ZL = 400Ω
Z0=100 Ω
fo = 300 Hz
Find:
  VSWR at flow = 150 Hz
  VSWR at fhigh = 450 Hz
  BW for VSWR <=1.5
  BW for VSWR <= 1.2

## Slide 5: Impedance Matching Techniques
Impedance matching using :
Lumped elements
Quarter-Wave transformer
Single-Stub Tuner
Double-Stub Tuner
Impedance matching is necessary to provide maximum delivery of RF power to load from source

## Slide 6: Single-Stub Matching

## Slide 7
A 50- T-L is terminated in an impedance of
ZL = 35 - j47.5. Find the position and length of the short-circuited stub to match it.
Normalize ZL
zL = 0.7 – j0.95
Find zL on S.C.
Draw  circle
Convert to yL
zL
yL
Find r=1 circle
Find intersection of  circle and r=1 circle (yB)
yB
Find distance traveled (WTG) to get to this admittance
WTG = .109
WTG = .168
This is dSTUB
dSTUB = (.168-.109)
dSTUB = .059

## Slide 8
Find bB
yB
bB = 1.2
Locate PSC
PSC
Set bSTUB = bB and find ySTUB = -jbSTUB
ySTUB = -1.2
Find distance traveled (WTG) to get from PSC to bSTUB
WTG = 0.25
WTG = 0.361
This is LSTUB
LSTUB = (0.361-0.25)
LSTUB = .111
Our solution is to place a short-circuited stub of length .111 a distance of .059 from the load.

## Slide 9
There is a second solution where the  circle and r=1 circle intersect. This is also a solution to the problem, but requires a longer dSTUB and LSTUB so is less desirable, unless practical constraints require it.
zL
yL
yB1
WTG = .109
yB2
WTG = .332
dSTUB = (.332-.109)
dSTUB = .223
LSTUB = (.25+.139) 
LSTUB = .389 

## Slide 10
A load of 100 + j150 ohm is connected to a 75 ohm lossless line. Find